## Slide 1
FMM 170317
MARIO PALMA

## Slide 2: Motivation
Similar results
Figure out the model that they used to fit the data
Differences between their system and our system

## Slide 3: Device and set up
CBT consist of
  22 parallel row
  33 junctions in series
CBT is electroplated with Cu
  Island (39x206x6.14µm3)
  (40000 µm3)
  B parallel to the long axis
Closed Ag box
Thermalization to the MC
PCB board with RLC-low pass filters
Ag coated bond wires
Cu wires connected to the filters placed on the MC
Notes: Area for my CBT????????

## Slide 4: Calibration
Calibration at 3 different temperatures at 2 different B fields.
Full fit of the conductance with: RT,CΣ, T
5T: RT=25.10 ± 0.06 kΩ; CΣ =191.9 ± 0.8fF
0.1T: RT=24.99 ± 0.06 kΩ; CΣ =192.4 ± 0.9fF
Secondary mode
TCBT=8.1 mK -> TMXC=7.1 mK after 5 hours
TCBT=9 mK -> TMXC=6.5 mK after 2 weeks
TCBT=8.1 mK -> TMXC=6.5 mK after 1 week
EC= 9.37 mK

## Slide 5: Demag
Precooling: Ti~9 mK; Bi =5T
Precooling time 14 hours!!!
Less thermal mass
Demag 5T->0.1T
ramp-rate: 2.5 mT/s(9T/hour)
Super fast ~ 4x
Overshoot
Adapt the ramp-rate
w/o SC heat-switch!!!

## Slide 6: DMR170306
9T-> 8T; 1T/h
8T->0.08T; 2T/h

## Slide 7: multi-rate
10 mT/s
2.5 mT/s
10 mT/s
2.5 mT/s
0.5 mT/s
2.5 T
1.5 T
Break at 1.4T
10 mT/s: Tf ~ 5 mK ;
hold time≪400s large overshoot
2.5 mT/s: Tf ~ 4.7 mK ;
hold time ~ 400s
multi-rate demag: Tf ~ 4.5 mK
hold time ~ 1000s
multi-rate demag: Tf ~ 4.5 mK
hold time ~ 1200s
multi-rate:
lower Tf
longer hold time

## Slide 8: DMR170313
9T->8T 1T/h(0.28mT/s); 8T->2T 2T/h(0.56mT/s);2T 3 hours break; 2T->0.4T 1T/h; 0.4T->0.08T 0.5T/h
Ti =21.5 mK; Tf =4.4 mK; hold time: 1170 s

## Slide 9: Model
Adiabatic Nuclear Demagnetization

## Slide 10: Model 2
Mario’s simulation
Ramp-rate 2.5 mT/s

## Slide 11: Model 3
Mario’s simulation
Assumptions: Qpar=6.317 fW;
Tp(t)=Tp(0)+2.960μK/s*t(???) eddy current heating
Effective volume ~ 12% island volume

## Slide 12: Conclusions
Cooling of the CBT below 5 mK (2.7 mK)
New cooling technique ( magnetic cooling for electronic nanodevices)
Multi-rate demag increase the hold time and decrease the lowest T
Efficient precooling down to 9 mK (23 mK)
Poor demag efficiency a factor 2 (ξ=4%) (8(ξ=37%))