## Slide 1
Approaching mK temperatures
in nanoscale devices
https://baselcryogenics.unibas.ch
baselcryogenics-physik@unibas.ch

## Slide 2: History and Company profile
https://baselcryogenics.unibas.ch
baselcryogenics-physik@unibas.ch
History
Publication: APL 104, 211106 (2014)
NCCR QSIT qstarter award (2014)
People
>100 Filters produced (mostly in-house use)
Product development: Low-T world record (2017)
BaselCryogenics Startup:
homepage https://baselcryogenics.unibas.ch (2015/2016)

## Slide 3: Low temperatures: Why?
https://baselcryogenics.unibas.ch
baselcryogenics-physik@unibas.ch
Temperature leads to blurring (temperature broadening, e.g. FD distribution)
Destroys fragile effects with small energy scale (novel phases)
Quasiparticle poisoning, decoherence (quantum computing)
=> Lower temperature  Microscope with better resolution

## Slide 4: Low temperatures: How? MC 100mK 1K 4K
https://baselcryogenics.unibas.ch
baselcryogenics-physik@unibas.ch
4 step process:
Proper shielding
Material choice
(low heat release / metal)
Filter leads (MW)
Thermalize leads
Our Filters:
Ultrastrong attenuation
Tight up to 50GHz
Small: 6mm*22mm
Ideal thermalizer: Long wire + conductive matrix
easy to cool/thermalize

## Slide 5: Results: Metallic coulomb blockade thermometer
https://baselcryogenics.unibas.ch
baselcryogenics-physik@unibas.ch
High resistance >100kW, cooling through leads not effective
Large Cu – islands => on chip nuclear demagnetization
Sample shield (Cu-box)
12cm Massive filter: 12cm, 0.3mm diam. Cu wire, Cu core
On Cu nucl.stage => on – off chip cooling: APL 111, 253105 (2017)
2.8 mK  World record

## Slide 6
https://baselcryogenics.unibas.ch
baselcryogenics-physik@unibas.ch
Thank you for your attention
Visit our webpage:
https://baselcryogenics.unibas.ch
Contact us:
baselcryogenics-physik@unibas.ch
(Google: Basel Cryogenics)
Cold electrons
Price:
1 Filter: 600 Eur
≥ 5 Filters: 510 Eur /pp
≥ 10 Filters: 400 Eur /pp